## Slide 1: Beacons
by Deeptiman Pattnaik

## Slide 2: What is a Beacon?
Beacon is a Bluetooth Low Energy signal transmitter used to communicate with any Bluetooth Low Energy devices in the proximity.
Bluetooth Low Energy Devices

## Slide 4: How it works?
It’s simple

## Slide 5: Beacon Technology
Chipset , Battery , Firmware

## Slide 6: Chipset
A board with combination of circuits , controllers , processors , switch and many electronic modules to perform a computation task.
Beacon Chipset Vendors

## Slide 7: Beacon Battery
Beacon also uses Alkaline battery with 2000 mAh power.
USB beacons don’t need battery replacement.
Beacons chipset uses Lithium coin cell battery with various power choice.

## Slide 8: Aislelabs Report

## Slide 9: Beacon Firmware
Beacon firmware consists of TX power , Advertising Interval , GATT profile.
Transmit Power
Beacon chipset has signal transmission power.
TX power measures by decibels milliwatt (dBm) unit. 1 mW = 0.001 W.
Higher the TX power , Longer the signal strength.
Lower the TX power , lower battery consumption.
Advertising Interval
The frequency rate at which a beacon transmit signal.
Higher the advertising interval , Higher the battery life.
If advertising interval 100ms means signal emit 10 times a single second.

## Slide 10: GATT (Generic Attribute Profile )
GATT defines a hierarchical data structure connected to BLE devices.
ALERT_NOTIFICATION_SERVICE
ALERT_LEVEL
ALERT_NOTIFICATION_CONTROL_POINT
ALERT_STATUS
Example

## Slide 11
That’s all in Hardware

## Slide 12: Beacon Protocol

## Slide 13
iBeacon introduced by Apple. It works on both iOS and Android platform. It allows app developers to code Beacons apps using the BLE APIs in both the platform.
iBeacon UUID (16 digit string number) with Major (4 digits) and Minor (4 digits).
iBeacon can transmit 31 bytes of data with a rate of 100ms advertising interval.

## Slide 14: iBeacon packet format
1A | FF | .. | . . | UUID (16 bytes) | Major | Minor | TX
Manufacturer Specific Data
4C00 | 02 | 15 | 585CDE931B0142CC9A1325009BEDC65E | 0000 | 0000 | C5
4C000215585CDE931B0142CC9A1325009BEDC65E000000005
Apple Company Identifier | 0x004c | -
Data Type | 0x02 | -
Data Length | 0x15 | 21
UUID | 585CDE931B0142CC9A1325009BEDC65E | -
Major | 0000 | -
Minor | 0000 | -
TX Power | 0xC5 | -59

## Slide 15
Eddystone standard introduced by Google.
Eddystone has three different format type : Eddystone – URL , Eddystone – UID , Eddystone – TLM.
Eddystone can transmit 31 bytes of data with a rate of 1-2sec advertising interval. So , this format beacons are more battery efficient.
03 | 03 | FEAA
… | 16 | FEAA | 00 | TX | Namespace ID (10 bytes) | Instance ID (6 bytes)
Service UUID
Service Data

## Slide 16: Eddystone packet format
8B0CA750-E7A7-4E14-BD99-095477CB3E77
8B0CA750 | 095477CB3E77

## Slide 17: Eddystone URL
http:// | g | o | o | . | g | l | / | y | I | x | w | E | w
02 | 67 | 6F | 6F | 2E | 67 | 6C | 2F | 79 | 49 | 78 | 77 | 45 | 77
http://goo.gl/yIxwEw
It’s a beacon broadcast format that send out URL to smartphone device.
The beacon signal can be read by Chrome browser widget or Physical Web beacon app in iOS and Android.
No need to code separate Beacon app , the URLs can be picked up in notification tab in smartphones.
Eddystone URL standard also knows as Physical Web.

## Slide 18: Eddystone TLM (Telemetry)
Eddystone TLM transmit sensor data like battery power , beacon temperature , time since device powered on and number of advertising packet transmit since powered on.
03 | 03 | FEAA
Service UUID
Service Data
.. | 16 | FEAA | 20 | … | BATT | TEMP | ADV_CNT | ELASPED

## Slide 20: Beacon in use
Beacons used in many real world scenarios like Hotels , Supermarket , Airport , Museum and many more

## Slide 21: Beacon Demo

## Slide 22: Reference
http://www.aislelabs.com/reports/beacon-guide/
https://newcircle.com/s/post/1786/2016/01/04/bluetooth-uuids-and-interoperable-advertisements
http://mindbowser.com/blog/what-is-internet-of-things-and-bluetooth-smart/
https://developer.bluetooth.org/gatt/services/Pages/ServicesHome.aspx?_ga=1.31027256.607688153.1461568231
https://www.youtube.com/watch?v=TZf4WquRGJU
https://www.youtube.com/watch?v=s-4J7cijPAo
http://stackoverflow.com/questions/17870189/android-4-3-bluetooth-low-energy-unstable
http://stackoverflow.com/questions/21398766/android-ble-connection-time-interval
http://stackoverflow.com/questions/27017224/why-the-app-doesnt-reconnect-to-the-ble-device-when-set-autoconnect-to-true-in
http://stackoverflow.com/questions/35903325/android-ble-characteristics-getvalue-returns-null/
http://stackoverflow.com/questions/35937529/how-to-transfer-data-between-two-android-devices-using-beacon
http://stackoverflow.com/questions/36054187/how-many-urls-can-be-written-to-a-physical-web-beacon/

## Slide 23: Thank you